Low Frequency Receiver
Flight Software Verification Report
Version 2.4
Solar Orbiter Mission
RPW INVESTIGATION
MEB (Main Electronic Box) Instrument
LFR (Low Frequency Receiver) Sub-Instrument

Name	Position	Signature
Paul LEROY	Technical manager / Flight Software Developer
Bruno Katra	Validation Team
Véronique Bouzid	Validation Team

Iss	Rev	Date	Author	Notes
1	0	11 JUL 2014	PLE	First issue
1	1	18 SEP 2014	PLE	REQ-LFR-SRS-5400 deleted / REQ-LFR-SRS-5403 not tested at LFR level / Requirements changed from “design” to test: / 5215, 5216, 5204, 5208, 5512, 5518 / JIRA RPWSWR-433 remarks taken into account
2	0	05 NOV 2015	NBR	FSW R3.0.0.10 + GCOV analysis
2	1	01 MAR 2016	BKA/VBO	FSW R3 UPDATED / Version of LFR FSW added in §1.2 / Requirements changed from “design” to test: / 5407 5409 5214 5237 5534 5536 5545 5546 5548 5508 5513 5514 5516 / 5202 5206 5210 5212 5241 5501 5540 5541 5542 5547 / Requirements Inspection added / 5544 5559 5560 5561 5800
2	2	15 MAY 2016	BKA/VBO	Several updated to be compliant with LESIA inspection review. / DOC5 added / DOC6 added / DOC7 added / §3.1 updated / §3.6 updated / §3.8 updated / §3.9 updated / §3.11 updated / §3.15 updated / §3.18 updated / §3.20 updated / §3.21 updated / §3.24 updated / §3.25 updated / §4.1 updated / §4.2 updated / §4.3 updated / §4.4 updated / §4.10 updated / §4.14 updated / §4.15 updated / §5.1 updated / §5.6 updated / Following JIRA issues have been taken into account : / RPWSSS-608, RPWSSS-607, RPWSSS-577, RPWSSS-588,RPWSSS-593, RPWSSS-598, RPWSSS-587, RPWSSS-589, RPWSSS-592, RPWSSS-586, RPWSSS-599, RPWSSS-600, RPWSSS-601,RPWSSS-596, RPWSSS-597, RPWSSS-584, RPWSSS-576
2	3	20 APRIL 2017	BKA	Quick recheck for R3++ compliancy / §1.2 updated / §2 Documents updated / §3.1 results updated / §3.6 updated (FSW version) / §3.8 updated (FSW version) / §3.9 updated (FSW version) / §3.11 updated (FSW version) / §3.15 updated / §3.18 updated / §3.20 updated / §3.21 updated / §3.25 updated / §4.1 results updated / §4.14 updated (FSW version)
2	4	14 AUGUST 2017	BKA	Updates for R3++ updated DP: / Applicable document version updated / §3.1 results updated / §3.12 updated / §3.17 updated (reference to detailed budget in SDD added) / §3.21 updated (typo in file names) / §4.1 results updated / §4.15 updated (FSW version) / §5.1 updated with memory map reference and RFW 225 approved / §5.2 updated / §5.4 updated / §5.5 updated
2	5	17 NOV 2018	VBO/BKA	§6 GCOV for 3.2.0.24

Table of Contents

# Introduction
## Purpose of the document
LFR is one of the three wave analyzers of the RPW consortium, which is a part of the Solar Orbiter instrument suite. The Laboratory of Plasma Physics (LPP) is in charge of the development and of the delivery of the LFR hardware and software jointly with the GSE, hardware and software.
The purpose of this document is to present the results of the LPP team verification activities performed on the LFR flight software.

## LFR FSW software version

The results presented in this document have been obtained with LFR FSW 3.2.0.15 (sources and software architecture) for R3++ campaign. Because no requirement tagged “Design ” or “Inspection” were introduced for R3++ campaign, this document contains just a quick recheck and non-regression updates.
# Documents
ID	Title	Reference
DOC1	LFR_Software_Acceptance_Test_Report002	RPW-SYS-MEB-LFR-RPT-000465-LES
DOC2	LFR Software Requirements Specification	RPW-MEB-LFR-SRS-00020	2.1
DOC3	RPW System Software Specification	RPW-SYS-SSS-00013-LES	4.3
DOC4	LFR Software ICD	RPW-SYS-MEB-LFR-ICD-00097	4.3
DOC5	LFR Software Development Plan	RPW-MEB-LFR-SDP-00040-2-2_LFR	2.2
DOC6	LFR Software Design Document	RPW‐MEB‐LFR‐SDD‐00039	1.4
DOC7	LFR Software User Manual	RPW-MEB-LFR-NTT-000123-LPP	1.5
DOC8	LFR_FSW-3-2-0-15_linker_script	RPW-MEB-LFR-RPT-00259_LPP	1.0

# R1 Requirements
## Summary of the requirements
REQ-LFR-SRS-	SSS-	Date	Verdict	Notes
5402	IF-DPS-EQ-070	14/08/2017	OK
5408	IF-DPS-EQ-170	14/08/2017	OK
5410	IF-DPS-EQ-200	14/08/2017	OK
5201	CP-FS-030	14/08/2017	OK
5235	CP-FS-033	14/08/2017	OK
5213	CP-FS-140	14/08/2017	OK
5538	CP-EQS-090	14/08/2017	OK
5539	CP-EQS-100	14/08/2017	OK
5559	CP-EQS-151	14/08/2017	OK	This is also partially verified by several test scenarii
5560	CP-EQS-152	14/08/2017	OK
5529	CP-EQS-520	14/08/2017	OK
5600	HR-EQ-040	14/08/2017	OK
5601	HR-EQ-050	14/08/2017	OK
5704	DR-001	14/08/2017	OK
5705	DR-003	14/08/2017	OK
5700	DR-010	14/08/2017	OK
5701	DR-020	14/08/2017	OK
5706	DR-025	14/08/2017	OK
5702	DR-030	14/08/2017	OK
5703	DR-040	14/08/2017	OK
5707	IR-010	14/08/2017	OK
5708	IR-020	20/04/2017	OK
51400	SM-100	20/04/2017	OK
51401	SM-110	20/04/2017	OK

## REQ-LFR-SRS-5402 / SSS-IF-DPS-EQ-070
SSS-IF-DPS-EQ-070 : DPU/Analyzer communication protocol: addressing method
The logical addressing method to identify the SpaceWire target destination in the SpaceWire
packets shall be used by the DPU Software and the RPW Analyzer FPGA firmware / flight
software.
Logical addressing method is used to access the LFR. The first byte of any CCSDS packet received by the LFR shall be equal to the LFR node address, 0xfe (function recv_task() in fsw_spacewire.c, data structure ccsdsTelecommandPacket_t in ccsds_types.h). Node address is kept in data structure spw_config defined in grspw.h
## REQ-LFR-SRS-5408 / SSS-IF-DPS-EQ-170
SSS-IF-DPS-EQ-170 : DPU / RPW Analyzer SW communication protocol
The SpaceWire communication protocol between the DPU Application Software and the RPW
analyzer flight software shall be the CCSDS packet transfer protocol as defined in ECSS-E-ST-50-53C.
The Space Wire communication protocol between the LFR flight software and the DPU is compliant with the LFR software ICD [DOC4]. The CCSDS packet transfer protocol is used. Space Wire FPGA IP and Space Wire device driver code for LEON-3 FT are provided by GAISLER Included. Full GAISLER code implementation is done in LFR FSW.
## REQ-LFR-SRS-5410 / SSS-IF-DPS-EQ-200

SSS-IF-DPS-EQ-200 : Data packets (RPW Analyzer SW to DPU SW) / The data (science data and non-science) generated by the Analyzer Flight Software shall be transmitted to the DPU Software as Telemetry Source Packets according to [ES1] with a maximum length given below for each equipment: / - LFR: SY_LFR_TM_MAX_LEN = 4112 bytes (i.e. 4096 bytes of application data)

The maximum length of the Telemetry Source Packets transmitted by the LFR toward the DPU is 4058 bytes. The longest packets are CWF_F1, 2 and 3 packets:
- protocol header	4	bytes
- header
  - PACKET_HEADER	16	bytes
  - AUXILIARY_DATA_HEADER	10	bytes
- /SOURCE_DATA/[…]/CWF_Fx	4032	bytes (336 * 12)
## REQ-LFR-SRS-5201 / SSS-CP-FS-030
SSS-CP-FS-030: Command management
The RPW Flight Software shall always process immediately the received command packets.
By design, the TC packets are processed by a dedicated RTEMS task which is executed as soon as the processor becomes available. The commands are always seen as immediate commands.
At program launch, Init function in fsw_init.c, create and run all other RTEMS tasks.
TC packets reception is handled by task named Task_id[TASKID_RECV]=”RECV”
Function recv_task() in fsw_spacewire.c decode SpW packets, check content and manage communication error then if packet is error free, it transmits TC to Action Task for immediate execution help of a message queue.
## REQ-LFR-SRS-5235 / SSS-CP-FS-033
SSS-CP-FS-033 : Command management EIDA R-191 / Each command packet shall contain one and only one command function, as specified in Solar Orbiter TM-TC and Packet Structure ICD .

Each TC packet handled by the LFR flight software contains only one command function.
Function tc_parser() in file tc_acceptance.c (in R3++ datapackage : 02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\ )parses TC packets, it checks process id, sid, category, length, type, subtype , cyclic redondancy check (CRC).
## REQ-LFR-SRS-5213 / SSS-CP-FS-140
SSS-CP-FS-140 : HK reporting EIDA R-197, AD5-PERP-1, AD5-PERP-6 / For the transmission of the housekeeping (to the DMS or to the DPU depending on the RPW subsystem that is initiator of the transmission), the RPW Flight Software shall implement the Housekeeping Parameter Report sub-service (sub-type = 25) of the PUS Housekeeping Reporting service (type = 3) as defined in [ES1] but with the following restrictions concerning the structure of the reports: / - All the parameters of the different HK reports shall be sampled once (i.e. copied one time in the HK report) per collection interval (i.e. per generation period). / - There is no fixed-length arrays.

For the transmission of the housekeeping to the DPU, the LFR flight software implements the Housekeeping Parameter Report sub-service (subtype = 25) of the PUS Housekeeping Reporting service (type = 3). See function init_housekeeping_parameters in fsw_misc.c, called by Init() from fsw_init.c : it collects constant HK parameters at real time task creation time, HK emission is a rate monotonic task. Function hous_task() in fsw_misc.c execute the data collection of variable HK parameters like packet sequence control, datation, HK fifo status, spacewire errors statistics, temperatures (LFR pcb, LFR fpga, SCM), common parameters, [V, e1, e2@F3=16Hz) and cpu load.

## REQ-LFR-SRS-5538 / SSS-CP-EQS-090

SSS-CP-EQS-090 : Equipment HK reporting / The generation period of the HK equipment report packets cannot be changed by command.

The generation period of the HK packets cannot be changed by telecommand (no existing TC for this purpose in [DOC4]).
A rate monotonic task created at FSW initialisation time is used to generate HK, each second, its name is Task_name[TASKID_HOUS]=“HOUS”.
( R3++ datapackage :	02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\fsw_init.c).
This task is launched and executed each second through the use of rtems_rate_monotonic_period function (R3++ datapackage :	02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\fsw_misc.c) with the constant HK_PERIOD which is set to 100 units of 10ms e.g. 1s (R3 datapackage :	02_Design_Definition_File\DDF.4_Source_code\header_3_2_0_15.zip\header\lfr_common_headers
fsw_params.h)
As soon as the flight software is launched, it sends HK reports each 1 s.
LFR FSW does not handle any exposed mechanism or backdoor to change HK period (Details of design justification can be found in [DOC6] at §7.5.4 )
## REQ-LFR-SRS-5539 / SSS-CP-EQS-100
SSS-CP-EQS-100 : Equipment HK reporting / The generation of the HK equipment reports cannot be disabled.

The generation of the HK reports cannot be disabled because :
- There is no existing TC for this purpose in [DOC4].
- It is done by a rate monotonic task called HOUS (created in R3++ datapackage : 02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\fsw_init.c) launched at FSW initialisation time.
- LFR FSW does not handle any exposed mechanism or backdoor to disable HK reporting (Details of design justification can be found in [DOC6] at §7.5.4 -> REQ-LFR-SRS-5539)

## REQ-LFR-SRS-5559 / SSS-CP-EQS-151
SSS-CP-EQS-151 SpaceWire link monitoring
The equipment flight software shall monitor the state of the Space Wire interface.
The Space Wire software is in fsw_spacewire.c. An interrupt subroutine is launched each time a space wire event happens at device driver level, two sub tasks are created to handle reception and emission through Space Wire interface. Function spacewire_compute_stats_offsets() is called each time a spw error occurs to maintain a persistent log of spacewire error, because SpaceWire driver error statistic report is deleted each time SpW driver is reset.
Without space wire error injection system, it is difficult to test driver error management, anyway LFR SGSE's HK pannel keeps track of all HK since power on, Space Wire interface health is monitored by Space Wire IF Statistics and Space Wire Error Counters list
Illustration 1: LFR SGSE HK from LFR model EQM-2 w FSW 3.0.0.8
Function spacewire_update_statistics() handles Space Wire Interface statistics ( receive, send, tick, time) and manage errors counters , i.e. Low severity Space Wire errors (parity , disconnect escape, synchro) and Medium Severity errors (early end of packet, invalid address, rx pckt truncation)
## REQ-LFR-SRS-5560 / SSS-CP-EQS-152
SpaceWire link monitoring: In case of detection of any SpaceWire failure (link errors, network level errors, ...) identified in 'RPW FDIR', the equipment flight software shall trace it in its periodic HK report.
HK are transmitted unconditionally by LFR every second, see LFR SGSE HK pannel screen-shot in Illustration 1: LFR SGSE HK from LFR model EQM-2 w FSW 3.0.0.8 and Illustration 2: LFR SGSE HK Pannel.
A dedicated task for HK handling (hous_task) is implemented in fsw_misc.c (in R3++ datapackage : 02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\). This task calls the 2 following functions which are defined in fsw_spacewire.c (in R3++ datapackage : 02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\) :
- spacewire_read_statistics  (reading of stats struct delivered through Spacewire driver)
- update_hk_with_grspw_stats (writing of relevant info in HK blocks)
Explanation and details concerning the stats and errors HK fields can be found in [DOC7] at §5.1.
## REQ-LFR-SRS-5529 / SSS-CP-EQS-520
SSS-CP-EQS-520: LFR data packets
The LFR flight software shall transmit the science data packets to the DPU as soon as the packets are ready, without having to wait for a request from the DPU (sporadic transmission).
The data packets are sent when they are ready without waiting for a request from the DPU. This is done through processing tasks described in [DOC6 - §5.7 and §5.8] :
- AVFx and PRCx tasks for science data packets of spectral products (ASM and BP)
- WFRM, CWF1, CWF2, CWF3 tasks for science data packets of waveform products (CWF and SWF)
## REQ-LFR-SRS-5600 / SSS-HR-EQ-040
SSS-HR-EQ-040 : RPW equipment hardware
To make possible the coexistence of the CCSDS protocol and RMAP protocol, the TDS, TNR-HFR and LFR equipment hardware shall be able to route the SpaceWire packets to the software in case of CCSDS packets or to the FPGA firmware in case of RMAP packets.

The routing of RMAP packets and CCSDS packets is done using the protocol identifier byte included in the protocol header. This byte is equal to 0x02 in case of a CCSDS packet and is equal to 0x01 is used for RMAP packets.
On the EM board, the transmission of RMAP packets has been done during TM transmission and the cohabitation worked well. This test has been ran on all posterior LFR models (systematic non regression verification).
## REQ-LFR-SRS-5601 / SSS-HR-EQ-050
SSS-HR-EQ-050 : RPW equipment hardware / After powering on or after a reset, the LEON3 processor of the analyzers shall enter in debug mode or halted mode without executing any instructions.

After powering on or after a reset, the LEON3 FT processor of LFR enters in halted mode without executing any instructions.
## REQ-LFR-SRS-5704 / SSS-DR-001
SSS-DR-001 : Design requirements and constraints EIDA R-236 / The RPW flight software shall be developed according to the standard [ES2].

The compliance of the development of the flight software with the ECSS E-ST-40 C has been verified by Software PA. Dedicated document named “ Follow-up Tailoring E40_v151106.xlsx ” is a traceability matrix that provides the LFR FSW standard compliance. It is delivered in R3, R3 updated and R3++ datapackages under following tree : \05_Product_Assurance_File\PAF.4_MX\.
## REQ-LFR-SRS-5705 / SSS-DR-003
SSS-DR-003 : Design requirements and constraints EIDA R-239 / The RPW DPU Application Software and the RPW Analyzer Flight Software shall reside in the DPU EEPROM (non-volatile memory).

The LFR flight software is not stored on board the LFR board. It is stored in the DPU EEPROM. The Remote Memory Access Protocol (RMAP) is used to upload LFR FSW from RPW DPU.

## REQ-LFR-SRS-5700 / SSS-DR-010
SSS-DR-010 : Design requirements and constraints EIDA R-052 / For each RPW flight software, the following margins for the estimates of processor load and memory occupation shall be met: / - 50% before/at PDR (i.e. the CPU load shall be less than 66%). / - 40% before CDR (i.e. the CPU load shall be less than 72%). / - 25% at FM AR (i.e. the CPU load shall be less than 80 %

The CPU load estimation is 65 % in the most demanding mode (SBM1), it is below 72 %.
CPU load is reported in HK, see Illustration 1: LFR SGSE HK from LFR model EQM-2 w FSW 3.0.0.8
Detailed CPU load can be found in §4.6 and §7.7 of [DOC6].
## REQ-LFR-SRS-5701 / SSS-DR-020
SSS-DR-020: Design requirements and constraints EIDA R-237 / The RPW flight Software shall have functionally distinct areas of memory assigned to: / - Code / - Fixed constants / - Variable parameters

The LFR flight software is delivered as two distinct files:
- .data srec => static data defined in the code
- .text srec => machine instructions which make up the program
  Source code is delivered in R3/R3updated/R3++ datapackages under following tree :
  \02_Design_Definition_File\DDF.4_Source_code
## REQ-LFR-SRS-5706 / SSS-DR-025
SSS-DR-025 : Design requirements and constraints EIDA R-255 / The RPW flight Software shall be structured in modules.

The flight software is structured in module., see §3.20 and §3.21
## REQ-LFR-SRS-5702 / SSS-DR-030
SSS-DR-030 : Design requirements and constraints EIDA R-241 / The RPW flight Software shall be structured such that modifications can be made to a software module without affecting other module positions in the memory.

The flight software is made of 16 C source file, each associated to a header file { fsw_config.c + fsw_globals.c + fsw_init.c + fsw_mis.c.c + fsw_processing_globals.c + fsw_spacewire.c + lfr_cpu_usage_report.c + tc_acceptance.c + tc_handler.c + tc_load_dump_parameters.c +tm_lfr_tc_exe.c + wf_handler.c + processing/avf0_prc0.c + /processing/avf1_prc1.c +processing.avf2_prc2.c + /processing/fsw-processing.c } , all source code have a small size so as object files. See paragraph below.
Source code is delivered in R3/R3updated/R3++ datapackages under following tree :
\02_Design_Definition_File\DDF.4_Source_code
## REQ-LFR-SRS-5703 / SSS-DR-040
SSS-DR-040 : Size of the flight SW executable image / The maximum size of the RPW flight SW executable image (trap table + .text section + .data section) is given below for each software: / − DBS: SY_DPU_DBS_EXE_MAX_SIZE = 64 kBytes / − DAS: SY_DPU_DAS_EXE_MAX_SIZE = 1200 kBytes / − LFR: SY_LFR_EXE_MAX_SIZE = 400 kBytes / − TDS: SY_TDS_EXE_MAX_SIZE = 400 kBytes / − TNR-HFR: SY_THR_EXE_MAX_SIZE = 400 kBytes

The R3++ FSW V3.2.0.15 binary image sizes contained in SREC files delivered in R3++ datapackage (\02_Design_Definition_File\DDF.5_Source_Product) are :
- .data section in RpwLfrApp_0013_data_rev-3-2-0-15.srec :	5008 bytes
- .text section in RpwLfrApp_0013_text_rev-3-2-0-15.srec	:	355 072 bytes
The section sizes are below the allocated sizes (400 kBytes for the LFR flight software).
## REQ-LFR-SRS-5707 / SSS-IR-010
SSS-IR-010	Implementation Requirements and Constraints
Concerning the Space Wire link implementation up to the packet and network levels, RPW FSW shall be compliant
Because Space Wire bus level instrumentation is required to generate or detect low-level errors, the compliance of the SpaceWire link implementation up to the packet and network levels to the following documents has not been checked,:
- ES1 Telemetry and telecommand packet utilization, ECSS-E-70-41A
- ES3 SpaceWire – Links, nodes, routers and networks, ECSS-E-ST-50-12C
- AD7 Solar Orbiter SpaceWire Application Protocol Specification SOL.S.ASTR.RS.00038
  By the way , LPP design team is confident in its Space Wire implementation, because:
- the compliance of Gaisler Space Wire IP is guaranteed by design
- the community of Gaisler Space Wire IP users did not alert about discrepancies
- the Star-Dundee Space Wire USB brick interface is compliant

LFR Flight Software House Keeping packets reports every second LFR status, eleven fields are devoted to Space Wire errors :

Illustration 2: LFR SGSE HK Pannel
## REQ-LFR-SRS-5708 / SSS-IR-020
SSS-IR-020 : Implementation requirements and constraints EIDA R-259 / The RPW flight Software shall be developed using a high-level language (C or C++).

The flight software has been developed using the C language, RTEMS Real-Time OS and Gaisler library. Details are given in [DOC5].
## REQ-LFR-SRS-51400 / SSS-SM-100
SSS-SM-100 : Flight software delivery format / The RPW flight SW executable image (.text section + .data section) shall be delivered to the PI team (LESIA) as a set of several files compliant to the SREC format. /  Separate files shall be provided for each .text section and each .data section.

The flight software is delivered as a set of several files compliant to the SREC format. One file is provided for the .data section and one file for the .text section.
This procedure has been tested and repeated since the LFR EM acceptance tests performed in July 2013 [DOC1].
See below FSW srec characteristics.
## REQ-LFR-SRS-51401 / SSS-SM-110
SSS-SM-110 : Flight software delivery format / The naming convention for the SREC files shall be the following: / − (RpwDasApp|RpwLfrApp|RpwTdsApp|RpwThrApp)_[0-9][0-9][0-9][0-9]_(text|data)(_[a-zA-Z0-9_-]*)?.srec / − [0-9][0-9][0-9][0-9] corresponds to a counter starting from 0001.

The two SREC files were delivered through dedicated JIRA issue (RPWSSS-197) in RpwLfrAppV3_2_0_15.zip file, 07/Apr/17. This is the R3.2.0.15 release of the LFR flight software , where srec files are:
- RpwLfrApp_0007_data_rev-3-2-0-15.srec
- RpwLfrApp_0007_text_rev-3-2-0-15.srec
Those files have been also delivered in “R3 ++”datapackage (may 2017) and are located in the following path inside datapackage : \02_Design_Definition_File\DDF.5_Source_Product

# R2 Requirements
## Summary of the requirements

REQ-LFR-SRS-	SSS-	Date	Verdict	Notes
5217	CP-FS-350	14/08/2017	OK
5221	CP-FS-400	14/08/2017	OK
5301	CP-FS-390	14/08/2017	OK
5223	CP-FS-455		POK	RFW 204
5224	CP-FS-460		NOK	RFW 204
5227	CP-FS-490		NOK	RFW 204
5228	CP-FS-495		NOK	RFW 204
5229	CP-FS-500		NOK	RFW 204
5306	IF-DPS-EQ-220	14/08/2017	OK
5307	IF-DPS-EQ-221	14/08/2017	OK
5401	IF-DPS-EQ-060	14/08/2017	OK
5510	IF-DPS-EQ-330	14/08/2017	OK
5544	CP-EQS-150	14/08/2017	OK
5561	CP-EQS-153	14/08/2017	OK

## REQ-LFR-SRS-5217 / SSS-CP-FS-350
SSS-CP-FS-350 : Time management EIDA R-405 / The format of the local time handled by the RPW Flight Software shall be compliant to the SCET format specified in [AD1]. / − The time pattern is made up of a coarse time part coded on 32 bits (number of seconds) and a fine time part coded on 16 bits (number of fractions of second). / − The resolution of the coarse time part is 1 second (least significant bit = 1 second). / − The resolution of the fine time part is 2-16 seconds (least significant bit = 15.2587891 μs)

The format of the local time handled by the LFR flight software is compliant to the SCTE format. The time pattern is made up of a coarse time part coded on 32 bits and a fine time part coded on 16 bits. The resolution of the coarse time part is 1 second. The resolution of the fine time part is 2^-16 second (15,2µs).
The bit 31 of the coarse time is reserved to synchronization management; it is equal to 1 if LFR is synchronized.
Implementation of this behaviour is exhaustively described id [DOC6]. However, this behaviour is also implicitely observed and verified during all the functional tests and calibration because correct implementation and resolution accuracy is mandatory for them. Concerning specifically the sync bit, it is implicitely verified during many tests (SVS-0011, SVS-0014, …).
## REQ-LFR-SRS-5221 / SSS-CP-FS-400
SSS-CP-FS-400 : Time management EIDA R-405 / The RPW Flight Software shall use its local time to timestamp all its internal events and all the data packets (HK data and science data). / - The RPW Flight Software local time value is copied in the S/C Time field of the TM packet data field header.

LFR uses its local time to time stamp all internal events and data packets. The LFR internal behaviour concerning time management is described in [DOC6] at §7.2.2 → “Time Management” ->REQ-LFR-SRS-5221.

## REQ-LFR-SRS-5301 / SSS-CP-FS-390
SSS-CP-FS-390 : Time management EIDA R-213 / Between two receipts of time-code and CTR message, the RPW Flight Software shall increment its local time autonomously with: / − a resolution of at least SY_RPW_TIME_RESOLUTION = 1 ms for the DAS and the three analyzers.

Between two received timecodes, LFR increments its local time autonomously with a resolution of 1/2^16 second. (15,2µs). The handling of local time is made at FPGA level, behaviour is described in [DOC6] at §7.3.
## REQ-LFR-SRS-5223 / SSS-CP-FS-455
SSS-CP-FS-455 : EDAC management / In case of a detection of an error (correctable or not correctable; on instruction or on data) by the EDAC, the LFR FSW shall report the error (including the failing address) by using its periodic HK. Not correctable bit errors are not seen by the EDAC (SSS-CP-FS-455 is partially covered).

LFR is shipped with a SRAM AEROFLEX UT8ER1M32M, it employs an embedded EDAC with user programmable auto scrubbing facility. The MBE pin, Multiple bit error, is asserted to prevent the host if multiple bit error happens during a read operation. LFR hardware does not handle the MBE signal, as LFR has no EEPROM memory usable to restore SRAM in case of corruption.
- If the error is correctable, correction will be done automatically by UT8ER1M32M, either at read time or during scrubbing task
- if the error is not correctable, LFR is not aware of SRAM corruption
- if SRAM is corrupted, LEON-3 FT cache – 4Ko code + 4 Ko data, which have an ECC mechanism, might be right, provided cache writing occurs prior to SRAM corruption
SSS-CP-FS-455 is partially covered
## REQ-LFR-SRS-5224 / SSS-CP-FS-460
SSS-CP-FS-460 : EDAC management / n case of detection of a correctable error, the LFR FSW shall scrub the failing memory location (write corrected data back). / UT8ER1M32M (master kind of SRAM) SRAM can automatically detect and correct a single bit word errors .

SRAM AEROFLEX UT8ER1M32M automatically corrects single bit word error in event of an upset,
UT8ER1M32M (master kind of SRAM) SRAM scrubbing period is set at boot time by FPGA:
- Scrub Rate Period is set to 15 (A[3..0]=15), so interval between scrub operation is 1,64ms
- interval between /Scrub and Busy is set to 14 (A[7..4]=14) so Busy state will change 700ns after /Scrub
- Bypass EDAC bit is false (A[8]=0, normal EDAC operations occur)
The SRAM EDAC register could be set by software.

## REQ-LFR-SRS-5227 / SSS-CP-FS-490
SSS-CP-FS-490 : EDAC management / The LFR FSW shall periodically scrub the entire memory area protected by EDAC (read, check memory status, write corrected data back).

 UT8ER1M32M (master kind of SRAM) SRAM scrubbing period is set at boot time by FPGA:
- Scrub Rate Period is set to 15 (A[3..0]=15), so interval between scrub operation is 1,64ms
- entire memory, made of two chips is checked every 524 288 * 1,64ms=1719,6”=859.8”=14.33’
- EDAC is done at each read operation
EDAC settings are programmable by software.
EDAC settings are also settable help of SocExplorer Software:
- Connect the SpaceWire Plugin to allow communication with LFR
- Using RegsExplorer panel, select “SRCTRLS-0WS”. This pannel, labeled “SRAM CONTROL” allows edition and modification of SRAM UT8ER1M32M EDAC setting
- Bit[3..0] sets Busy to Scrub Rate Period, values are {0:0ns, 1:50ns,….,15:750ns}
- Bit[7..4] sets Scrub Rate Period, values are {3:600ns, 4:1µs, 5:1.8µs,…. ,15:1.64ms}
- Bit 8: set EDAC in Run state
- Bit 9: bypass/BUSY signal
- Bit 10: write: enable SRAM settings, Read: indicates SRAM settings

## REQ-LFR-SRS-5228 / SSS-CP-FS-495
SSS-CP-FS-495 : EDAC management / The atomicity of the scrubbing actions (read / write back cycle) shall be guaranteed.

The atomicity of the scrubbing actions (read / write back cycle) is guaranteed by design of UT8ER1M32M SRAM
Please see ams.aeroflex.com/pagesproduct/datasheets/UT8ER2M32SRAMMCM.pdf
## REQ-LFR -SRS-5229 / SSS-CP-FS-500
The LFR FSW shall maintain a counter of the correctable errors and a counter of the not correctable errors detected by EDAC. These counters are part of the HW status reported in the periodic HK reports.

LFR FSW does not poll SRAM's MBE pin nor generate Interrupt Service Routine when MBE gets true, LFR Hardware does not count nor register Multiple Bit Error events. As FSW is stored exclusively in SRAM, there is no way to restore a valid context without shutting down LFR and upload FSW through RMAP protocol.
This requirement is not supported by LFR design.

## REQ-LFR-SRS-5306 / SSS-IF-DPS-EQ-220
SSS-IF-DPS-EQ-220 : Data packets (RPW Analyzer SW to DPU SW) / The Analyzer Flight Software shall support a data transmission scheme where the maximum wait time between acquisitions of the data packets by the DPU Software is given below for each equipment: / − LFR: SY_LFR_TM_MAX_OUTAGE = 10 ms / − TNR-HFR: SY_THR_TM_MAX_OUTAGE = 10 ms / − TDS: SY_TDS_TM_MAX_OUTAGE = 10 ms

By design, LFR has internal buffers that allow the storage of several seconds of data, this is sufficient to support a data transmission scheme where the maximum wait time between acquisitions of the data packets by the DPU software is SY_LFR_TM_MAX_OUTAGE = 10 ms. Here is a calculation in the worst case scenario e.g. during SBM1 mode which is the most intensive mode for data transmission :
- We consider a 1 second range of production where LFR FSW sends all products of SBM1 + SWF, ASM and BP of NORMAL mode = 56 packets e.g. 56x10ms = 560ms
- We add the effective transmission time : size of the 56 packets is 1393552 bits e.g. ~140ms at 10Mb/s datarate.
→ We obtain in consequence a maximum latency of 700ms which is below the several seconds that LFR internal buffers can store.
File fsw_processing.c manages memory rings for spectral matrices averaging and storage.
## REQ-LFR-SRS-5307 / SSS-IF-DPS-EQ-221
SSS-IF-DPS-EQ-221 : LFR Boot Parameters / The LFR boot parameters are the following: / − LFR RAM start address: SY_LFR_RAM_LOW_ADDR = 0x40000000 / − LFR RAM size: SY_LFR_RAM_SIZE = 0x00400000 / − LFR stack pointer address: SY_LFR_STACK_POINTER = 0x403FFFF0 / − LFR last reset reason configuration flag: SY_LFR_RESET_CAUSE_CONFIG = FALSE / − LFR last reset reason address: SY_LFR_RESET_CAUSE_ADDR = 0x00000000 / − LFR MCFG1 register value: SY_LFR_MCFG1 = 0x000002ff / − LFR MCFG2 register value: SY_LFR_MCFG2 = 0x00000e60 / − LFR MCFG3 register value: SY_LFR_MCFG3 = 0x00000000 / − LFR MCFG register configuration flag (TRUE = registers to be configured / FALSE = registers not to be configured): SY_LFR_MCFG_CONFIG = TRUE / − LFR FPU configuration flag (TRUE = a FPU is present / FALSE = no FPU): SY_LFR_FPU_CONFIG = TRUE / − LFR scaler reload register address: SY_LFR_SCALER_RELOAD_ADDR = 0x80000304 / − LFR scaler reload register value: SY_LFR_SCALER_RELOAD_VALUE = 0x00000018 / − LFR Timer1 reload register address: SY_LFR_TIMER1_RELOAD_ADD = 0x80000314 / − LFR Timer1 control register address: SY_LFR_TIMER1_CTRL_ADDR = 0x80000318 / − LFR AHB register configuration flag (TRUE = registers to be configured / FALSE = registers not to be configured): SY_LFR_AHB_CONFIG = FALSE / − LFR AHB status register address: SY_LFR_AHB_STATUS_ADDR = 0 / − LFR AHB failing register address: SY_LFR_AHB_FAILING_ADDR = 0 / − LFR watchdog configuration flag (TRUE = registers to be configured / FALSE = registers not to be configured): SY_LFR_WATCHDOG_CONFIG = FALSE / − LFR watchdog register address (significant if SY_LFR_WATCHDOG_CONFIG = TRUE): SY_LFR_WATCHDOG_ADDR = 0 / − LFR RAM wash flag: SY_LFR_RAM_WASH_CONFIG = TRUE / − LFR RAM wash delay: SY_LFR_RAM_WASH_DELAY = 2000 ms / − LFR RAM wash register: SY_LFR_RAM_WASH_ADDR = 0x80000000 / − LFR RAM wash register: SY_LFR_RAM_WASH_VALUE = 0x80000000

The LFR boot parameters are the following (some values are based on the VHDL design version 1.1.89 as delivered with the EM board jointly with the flight software 3.0.0.10):
- RAM start address = 0x40000000
- RAM size = 0x00400000
- stack pointer address = 0x403ffff0
- last reset reason configuration flag = Not Implemented
- last reset reason address = Not Implemented
- MCFG1 register value = 0x000002ff
- MCFG2 register value = 0x00000e60
- MCFG3 register value = 0x00000000
- MCFG register configuration flag = true (registers to be configured)
- FPU configuration flag = true (FPU is present)
- scaler reload register address = 0x80000304
- scaler reload register value = 0x00000018
- Timer1 reload register address = 0x80000314
- Timer1 control register address = 0x80000318
- AHB register configuration flag = false (registers not to be configured, not implemented on the EM VHDL design)
- AHB status register address = 0
- AHB failing register address = 0
- watchdog configuration flag = false (registers not to be configured)
- watchdog register address = 0
  Note: first number of VHDL version identifier identify the target technology: bitstream for RTAX-4000-D-1 is labelled 3.1.89, bitstream for A3PE-3000 is labelled 1.1.89 or 0.0.89 according to LFR model
## REQ-LFR-SRS-5401 / SSS-IF-DPS-EQ-060
SSS-IF-DPS-EQ-060 : DPU/Analyzer SpW interface / The RPW Analyzer Flight Software (TNR-HFR, TDS, LFR) shall handle the SpaceWire time-code generated by the DPU.

The SpaceWire IP instantiated in the LFR FPGA handles timecodes. The value of the last valid timecode is written in the LFR HK packets (HK_LFR_DPU_SPW_LAST_TIMC field) by flight software 3.0.0.0 and later (this validated by test SVS-0012).
 However, the timecode reception is used in the VHDL design to synchronize the LFR hardware with the timecodes sent by the DPU via the SpaceWire link.

## REQ-LFR-SRS-5510 / SSS-CP-EQS-330
SSS-CP-EQS-330 : Acquisition synchronization REQ-RPW-SYS-0201 / The equipment flight software shall allow to adjust the equipment sampling times by using its internal time (which is synchronized on the spacecraft clock) and the reference time that is transmitted as a parameter of the mode activating command.

LFR uses its local time and the reference time transmitted as a parameter of the TC_LFR_ENTER_MODE telecommand sent to engage the mode transition to start the acquisitions.

## REQ-LFR-SRS-5544/ SSS-CP-EQS-150
SSS-CP-EQS-150 : Equipment command feedback / The equipment flight software shall produce, depending on the final status of the execution and the possible encountered errors, the following command acknowledgment packets (which are compliant to the PUS service n°1): / - TM_LFR_TC_EXE_SUCCESS in case of execution success. / - TM_LFR_TC_EXE_CORRUPTED in case of error detected during the acceptance stage verifications (Illegal APID, Illegal packet type, Illegal packet subtype, wrong CRC, wrong or incomplete length). / - TM_LFR_TC_EXE_INCONSISTENT in case of wrong or inconsistent field in the data fields. / - TM_LFR_TC_EXE_NOT_EXECUTABLE in case of command that can not be executed at this time. / - TM_LFR_TC_EXE_NOT_IMPLEMENTED in case of command not implemented. / - TM_LFR_TC_EXE_ERROR if a malfunction or an error is detected during the execution.

Only TM_LFR_TC_EXE_ERROR is validated by inspection. The others TM_LFR_TC_EXE_xxx are validated by test (SVS-0059). Visible in tc_handler.c and tm_lfr_tc_exe (in R3++ : 02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\)

## REQ-LFR-SRS-5561/ SSS-CP-EQS-153
SSS-CP-EQS-153 : SpaceWire link monitoring After the loss of the SpaceWire connection, if the analyzer has failed to (re-)establish the connection with the DPU within a SY_xxx_DPU_CONNECT_TIMEOUT timeout period, then the equipment flight software shall:  - Reset the SpaceWire interface.  - Reset the connection timeout period.  - Start again the connection process.

Only requirements in bold are validated by inspection.

As described in [DOC6] at §5.2.2, the task that handled Spacewire interruption is called SPIQ (spiq_task) in fsw_spacewire.c (in R3 datapackage : 02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\). The following dedicated functions are used :
- spacewire_several_connect_attemps (handling of SY_LFR_DPU_CONNECT_TIMEOUT)
- spacewire_stop_and_start_link (Spacewire interface reset)

Behaviour is described exhaustively in [DOC6] at §7.5.7, it mainly consists in the call of rtems_task_wake_after(SY_LFR_DPU_CONNECT_TIMEOUT) function to reset connection timeout period and call of spacewire_stop_and_start_link for Spacewire interface reset.

# R3 Requirements
## Summary of the requirements

REQ-LFR-SRS-	SSS-	Date	Verdict	Notes
5225	CP-FS-470		NOK	Not Validated so RFW 204 still applicable
5226	CP-FS-480		NOK	RFW 204
5231	CP-FS-530	14/08/2017	OK
5232	CP-FS-540	14/08/2017	OK	RFW 225 approved on 29/06/2017
5800	OR-050	14/08/2017	OK	Memory map is delivered as an annex reference document [DOC8]

## REQ-LFR-SRS-5225 / SSS-CP-FS-470
SSS-CP-FS-470 EDAC management / In case of detection of a not correctable error during instruction fetch (instruction access error), the LFR FSW shall performed the actions specified in AD12

For now, non correctable error are not detected, hence no detection nor isolation nor recovery action can be done. Provided LEON 3 Fault Tolerant processor allows detection of a non correctable error at fetch time, this requirement may be implemented in LFR FSW version > R3+ . A Red Mine Issue is opened at LPP .
## REQ-LFR-SRS-5226 / SSS-CP-FS-480
SSS-CP-FS-480 EDAC management / In case of detection of a not correctable error during data access (data access exception); depending on the criticality of the data, the LFR FSW shall perform the actions specified in / AD12.

## REQ-LFR-SRS-5231 / SSS-CP-FS-530
SSS-CP-FS-530 Watchdog management / When the watchdog functionality is enabled, the LFR FSW shall periodically reload the watchdog counter before this one reaches zero and makes the system reset.

LFR FSW implements a software watchdog always enabled through an RTEMS task called “LOAD”. Countdown timer is configured to 10s and is reloaded every 1s by “LOAD” task. Functions related to watchdog implementation are located in fsw_misc.c (in R3++ datapackage : 02_Design_Definition_File\DDF.4_Source_code\src_3_2_0_15.zip\src\).
## REQ-LFR-SRS-5232 / SSS-CP-FS-540
SSS-CP-FS-540 Watchdog management / When the watchdog reaches 0, the LFR FSW shall activate a software context back-up procedure.

LFR FSW has no back-up procedure : when watchdog counter reaches 0, LFR FSW performs an exit(0)
RFW 225 has been approved by CNES on 29/06/2017.

## REQ-LFR-SRS-5800/ SSS-OR-050
SSS-OR-050 / Each analyzer flight software shall have its own user manual (SUM) covering the following points: - General description - Initialization phase - Modes and transitions - Housekeeping parameters and reports - Configuration (role of each configuration parameter that can be changed by TC) - Memory map (including physical mapping of SW onto subsystem HW) - Description of the science products (TM packets, auxiliary parameters, ...) - Data rates - Data time-stamping policy - Failures

The document nomenclature is RPW-MEB-LFR-NTT-000123-LPP-01-04_Software_User_Manual.
Memory map will be delivered in next release of [DOC6] and will be referenced in [DOC7]
# LFR FSW version 3.2.0.24 GCOV Analysis

## Software used

GCOV LESIA	GCOV LESIA code ingested into LPP's Code Repositories. / https://hephaistos.lpp.polytechnique.fr/rhodecode/HG_REPOSITORIES/LPP/INSTRUMENTATION/USERS/JEANDET/LFR_FSW/libgcov / Specific python scripts developped by A. Jeandet / record_lfr_console.py : retrieve , split data on EM board into a txt file / build_gcov_files.py : read the txt file and rebuild the file(gcda) / gcovr.py : generate html report / Warning : the same server hosts / - the LFR-FSW compiled with gcov options / - the files generated by record_lfr_console.py
LFR-FSW	LFR FSW code ingested into LPP's Code Repositories / https://hephaistos.lpp.polytechnique.fr/rhodecode/HG_REPOSITORIES/LPP/INSTRUMENTATION/USERS/JEANDET/LFR_FSW

        Generation of LFR FSW GCOV instrumented

To instrument our code we added compilations options on gcc
 "-fprofile-arcs -ftest-coverage"

List of files making up LFR FSW

FOLDER	FILES
header	*.h
src	fsw_init.c
	fsw_misc.c
	fsw_spacewire.c
	lfr_cpu_usage_report.c
	tc_acceptance.c
	tc_handler.c
	tc_load_dump_parameter.c
	tm_lfr_tc_exe.c
	wf_handler.c
src/processing	avf0_prc0.c
	avf1_prc0.c
	avf2_prc0.c
	fsw_processing.c
LFR_basic-parameters	basic_parameters.c / *.h

        Running LFR FSW GCOV instrumented

For this step, we need to use
- USB port (UART)
- the script record_lfr_console.py.
- TC_LFR_RESET ( Socexplorer GUI)
This command will be used to dump the data in hexa format via UART in a file named gcov_out_AAAA-MM-DD HH:MM:SS.zzzzzz.txt, which will be analyze by an other script build_gcov_file.py.

First of all
1- plug the USB cable between the LFR-EM board and USB hub.

2- Launch in a terminal and
cd /opt/VALIDATION_R3plusplus/GCOV
./record_lfr_console.py -p /dev/ttyUSB1 -s 115200

3-Launch Socexplorer and the SVS test.

4- At the end of the test, send a TC_LFR_RESET to dump the data (see below).

5- Move the gcov_out_AAAA_MM_DD*.txt into the SVS test folder

        LFR FSW GCOV Analysis Results

One folder by test and each test is associated with a gcov_out_xxx file. First we read the txt file and rebuild the file (gcda) test by test then we merge all files ( format gcda) to obtain global GCOV cover with gcovr.py script. HTML reports are generated.

The root Folder is GCOV_3.2.0.24

Environment variables are
SGCOV : path to libgcov
DBUILD : path to LFR FSW code compiled into Qt workspace
DTEST : path to root folder

Go to the top of the GCOV folder
cd ${DTEST}/GCOV_3.2.0.24

To generate html report GCOV for each SVS TEST:

1- Generate gcda files / txt file gcov_put_xxxxx.txt
${SGCOV}/build_gcov_files.py -r ${BUILD} -o ${DTEST}/SVS-xxxx/ ${DTEST}/SVS-xxxx/gcov_out_xxxxx.txt

Creation of src folder into the SVS test folder.

FOLDER	FILES
./	fsw_init.c.[gcda,gcno]
	fsw_misc.c.[gcda,gcno]
	fsw_spacewire.c.[gcda,gcno]
	lfr_cpu_usage_report.c.[gcda,gcno]
	tc_acceptance.c.[gcda,gcno]
	tc_handler.c.[gcda,gcno]
	tc_load_dump_parameter.c.[gcda,gcno]
	tm_lfr_tc_exe.c.[gcda,gcno]
	wf_handler.c.[gcda,gcno]
./processing	avf0_prc0.c.[gcda,gcno]
	avf1_prc0.c.[gcda,gcno]
	avf2_prc0.c.[gcda,gcno]
	fsw_processing.c.[gcda,gcno]
__/LFR_basic-parameters	basic_parameters.c.[gcda,gcno]

2- generate html report
cd ${DTEST}/SVS-xxxx
../../LFR_FSW/libgcov/gcovr.py -s ../../LFR_FSW -o . -g /opt/rtems-4.10/bin/sparc-rtems-gcov .

18 Html reports are generated,
- one global file named gcov.html
- one by file (gcda) named gcov_src_xxxxxx.c.html , ie gcov.src_processing_avf0_prc0.c.html
- one by header file header_GscMemoryLPP.hpp.html, header_processing_fsw_processing.h.html,
  LFR_basic-parameters_basic_parameters.h.html

To generate global html GCOV report
cd ${DTEST}/GCOV_3.2.0.24
../LFR_FSW/libgcov/gcovr.py -s ../LFR_FSW -o . -g /opt/rtems-4.10/bin/sparc-rtems-gcov .

Résulats
Lines 95.7%
Branches 85.2%