Spectral Matrix Calibration

It concerns the LFR 5x5 electromagnetic spectral matrices, either ASM or BP2, with three magnetic and two electric components:
stack{ {bold "SM"}^"L1"(%ioméga_j^(m)) ~=~ left langle left[ matrix{ nospace{B_1 B_1^"*"} # nospace{B_1 B_2^"*"} # nospace{B_1 B_3^"*"} # nospace{B_1 E_1^"*"} # nospace{B_1 E_2^"*"} ## cc # nospace{B_2 B_2^"*"} # nospace{B_2 B_3^"*"} # nospace{B_2 E_1^"*"} # nospace{B_2 E_2^"*"} ## cc # cc # nospace{B_3 B_3^"*"} # nospace{B_3 E_1^"*"} # nospace{B_3 E_2^"*"} ## cc # cc # cc # nospace{E_1 E_1^"*"} # nospace{E_1 E_2^"*"} ## cc # cc # cc # cc # nospace{E_2 E_2^"*"}} right] right rangle }

        (1)

where m is for F=0, 1 or 2, and j is a frequency index; they will hereafter be omitted throughout the text. The symbol * denotes the complex conjugate.

1. Data from the magnetic field sensor (SCM)

Let {bold "H"}(%ioméga) be the 3D-magnetic field vector in physical unit (nT) that the search coil magneto-meter feels, i.e. the SCM input, and {bold "J"}_{SCM}(%ioméga) be the corresponding SCM output in enginee-ring unit (V). The relationship between these two vectors defines the transfer matrix of SCM:
alignl ~~~~~{bold "J"}_{SCM}(%ioméga) `=` left[ matrix{ J_{1}(%ioméga) ## J_{2}(%ioméga) ## J_{3}(%ioméga)} right]_{SCM} ~=~ {overline overline bold "M"}_{JH}(%ioméga) cdot {bold "H"}(%ioméga) ~=~ left[ matrix{ C_{nospace{11}}(%ioméga) # C_{nospace{12}}(%ioméga) # C_{nospace{13}}(%ioméga) ## C_{nospace{21}}(%ioméga) # C_{nospace{22}}(%ioméga) # C_{nospace{23}}(%ioméga) ## C_{nospace{31}}(%ioméga) # C_{nospace{32}}(%ioméga) # C_{nospace{33}}(%ioméga)} right]_{SCM} cdot~ left[ matrix{ H_{1}(%ioméga) ## H_{2}(%ioméga) ## H_{3}(%ioméga)} right]_{SCM}

Here the indexes 1, 2, 3 refer to the SCM B1-B2-B3 axis system.

B1
B2
B3
LFR

JSCM (V)
BLFR (count)
H (nT)

The electric signals J_{1}(%ioméga), J_{2}(%ioméga), J_{3}(%ioméga) are injected into LFR as inputs. Let B_{1}(%ioméga), B_{2}(%ioméga), B_{3}(%ioméga) be the corresponding output signals; they are thus in count unit. Similarly there is a LFR transfer matrix that defines their relationship between them:
alignl ~~~~~{bold "B"}_{LFR}(%ioméga) `=` left[ matrix{ B_{1}(%ioméga) ## B_{2}(%ioméga) ## B_{3}(%ioméga)} right]_{LFR} ~=~ {overline overline bold "M"}_{BJ}(%ioméga) cdot {bold "J"}_{SCM}(%ioméga) ~approx~ left[ matrix{ R_{nospace{11}}^{SCM}(%ioméga) # 0 # 0 ## 0 # R_{nospace{22}}^{SCM}(%ioméga) # 0 ## 0 # 0 # R_{nospace{33}}^{SCM}(%ioméga)} right]_{LFR} cdot~ left[ matrix{ J_{1}(%ioméga) ## J_{2}(%ioméga) ## J_{3}(%ioméga)} right]_{SCM}
alignr {bold "B"}_{LFR}(%ioméga) ~=~ {overline overline bold "M"}_{BJ}(%ioméga) cdot {overline overline bold "M"}_{JH}(%ioméga) cdot {bold "H"}(%ioméga) newline dlrarrow ~~~~ {bold "H"}(%ioméga) ~=~ {overline overline bold "M"}^{-1}_{JH}(%ioméga) cdot {overline overline bold "M"}^{-1}_{BJ}(%ioméga) cdot {bold "B"}_{LFR}(%ioméga) Hence:

        (2)

Let’s note then {overline overline bold "M"}_{BH} ~=~ {overline overline bold "M"}_{BJ} cdot {overline overline bold "M"}_{JH} and {overline overline bold "M"}^{-1}_{BH} ~=~ {overline overline bold "M"}^{-1}_{JH} cdot {overline overline bold "M"}^{-1}_{BJ}

The transformation matrices from UARF to SRF and from SCM to UARF coordinates, are:
{overline overline bold "M"}_nospace{SRF -UARF} ~=~ left[ alignr matrix{ 0.501 # 0.600 # -0.624 ## 0.744 # -0.667 # -0.0437 ## -0.442 # -0.442 # -0.780} right] {overline overline bold "M"}_nospace{UARF-SCM} ~=~ left[ alignr matrix{ 0 # 0 # 1 ## 1 # 0 # 0 ## 0 # 1 # 0} right]
     (3)

2. Data from the electric field sensor (ANT/BIAS)

Let {bold "D"}(%ioméga) be the 2D-electric field vector in physical unit (V/m) that the electric antenna system feels, i.e. the ANT input, and {bold "V"}_{ANT}(%ioméga) be the corresponding ANT output in enginee-ring unit (V). The relationship between these two vectors defines the transfer matrix of ANT:
alignl ~~~~~{bold "V"}_{ANT}(%ioméga) `=` left[ matrix{ V_{12}(%ioméga) ## V_{23 }(%ioméga)} right]_ANT ~=~ {overline overline bold "M"}_{VD}(%ioméga) cdot {bold "D"}(%ioméga) ~=~ left[ matrix{ A_{nospace{1Y'}}(%ioméga) # A_{nospace{1Z'}}(%ioméga) ## A_{nospace{2Y'}}(%ioméga) # A_{nospace{2Z'}}(%ioméga)} right]_{nospace{SRF'}} cdot left[ matrix{D_{nospace{Y'}}(%ioméga) ## D_{nospace{Z'}}(%ioméga)} right]_{nospace{SRF'}}

The SRF’ frame is defined as the extension of the SRF frame where the Y’Z’ plane is the effective plane of electric field measurements. It should in principle not differ much if not at all from the SRF frame. In first approximation one may consider the following:

ANT 1
ANT 2
ANT 3

V23 = V2- V3
V12 = V1- V2
L12eff ~ L12 / 2
L23eff ~ L23 / 2
A1Y’ ~ +3.5 m
A1Z’ ~ -7.0 m
A2Y’ ~ -7.0 m
A2Z’ ~ 0.0

The indexes 1, 2 in the transfer matrix refer to the two differential potential measurements:
stack{V_{12}(%ioméga) ~=~ V_{1}-V_{2} # V_{23}(%ioméga) ~=~ V_{2}-V_{3}}

left[ matrix{D_{nospace{Y'}}(%ioméga) ## D_{nospace{Z'}}(%ioméga)} right]_{nospace{SRF'}} ~=~ size18{alignc 1 over {A_{nospace{1Y'}}A_{nospace{2Z'}}-A_{nospace{1Z'}}A_{nospace{2Y'}}}} left[ matrix{A_{nospace{2Z'}}(%ioméga) # -A_{nospace{1Z'}}(%ioméga) ## -A_{nospace{2Y'}}(%ioméga) # A_{nospace{1Y'}}(%ioméga)} right]_{nospace{SRF'}} cdot left[ matrix{ V_{12}(%ioméga) ## V_{23}(%ioméga)} right] Thus:

{overline overline bold "M"}_{VD}^{-1} ~simeq~ left[ matrix{0. # -0.143 ## -0.142 # -0.071} right] (m^{-1} )

left[ matrix{D_{nospace{Y'}}(%ioméga) ## D_{nospace{Z'}}(%ioméga)} right]_{nospace{SRF'}} ~simeq~ left[ matrix{V_{23} `/ ` A_{nospace{2Y'}} ## (V_{12} + V_{23}/2) `/` A_{nospace{1Z'}}} right]

Then, the electric signals V_{12}(%ioméga), V_{23}(%ioméga) are injected into BIAS as inputs. Let K_{1}(%ioméga), K_{2}(%ioméga) be the corresponding BIAS output signals still in engineering unit (V). The relationship between them defines the transfer matrix of BIAS:
alignl ~~~~~{bold "K"}_{BIAS}(%ioméga) `=` left[ matrix{ K_{1}(%ioméga) ## K_{2}(%ioméga)} right]_BIAS ~=~ {overline overline bold "M"}_{KV}(%ioméga) cdot {bold "V"}_{ANT}(%ioméga) ~approx~ left[ matrix{ B_{nospace{11}}(%ioméga) # 0 ## 0 # B_{nospace{22}}(%ioméga) } right]_{BIAS} cdot~ left[ matrix{ V_{12}(%ioméga) ## V_{23}(%ioméga) } right]_{ANT}

ELFR (count)
LFR

VANT (V)
D (V/m)

BIAS

KBIAS (V)

The electric signals K_{1}(%ioméga), K_{2}(%ioméga) are injected into LFR as inputs. Let E_{1}(%ioméga), E_{1}(%ioméga) be the corresponding output signals; they are thus in count unit. Similarly there is a LFR transfer matrix that defines their relationship between them:
alignl ~~~~~{bold "E"}_{LFR}(%ioméga) `=` left[ matrix{ E_{1}(%ioméga) ## E_{2}(%ioméga) } right]_{LFR} ~=~ {overline overline bold "M"}_{EK}(%ioméga) cdot {bold "K"}_{BIAS}(%ioméga) ~approx~ left[ matrix{ R_{nospace{11}}^{BIAS}(%ioméga) # 0 ## 0 # R_{nospace{22}}^{BIAS}(%ioméga) } right]_{LFR} cdot~ left[ matrix{ K_{1}(%ioméga) ## K_{2}(%ioméga) } right]_{BIAS}

alignr {bold "E"}_{LFR}(%ioméga) ~=~ {overline overline bold "M"}_{EK}(%ioméga) cdot {overline overline bold "M"}_{KV}(%ioméga) cdot {overline overline bold "M"}_{VD}(%ioméga) cdot {bold "D"}(%ioméga) newline dlrarrow ~~~~ {bold "D"}(%ioméga) ~=~ {overline overline bold "M"}^{-1}_{VD}(%ioméga) cdot {overline overline bold "M"}^{-1}_{KV}(%ioméga) cdot {overline overline bold "M"}^{-1}_{EK}(%ioméga) cdot {bold "E"}_{LFR}(%ioméga) Hence:
        (4)

Let’s note then {overline overline bold "M"}_{ED} ~=~ {overline overline bold "M"}_{EK} cdot {overline overline bold "M"}_{KV} cdot {overline overline bold "M"}_{VD} and {overline overline bold "M"}^{-1}_{ED} ~=~ {overline overline bold "M"}^{-1}_{VD} cdot {overline overline bold "M"}^{-1}_{KV} cdot {overline overline bold "M"}^{-1}_{EK}

3. Calibration operations to be performed on the ground

3.1. Magnetic field data in SCM B1-B2-B3 axis system and electric field data in ANT Y’-Z’ SRF

From Eqs. (1), (2) and (4), the 5x5 electromagnetic spectral matrices to be calibrated can thus be written as follows:

{bold "SM"}^"L1" ~=~ left langle ~left[ matrix{ B_{nospace{1}} ## B_{nospace{2}} ## B_{nospace{3}} ## E_{nospace{1}} ## E_{nospace{2}} } right] cdot left[ matrix{B_{nospace{1}}^"*" # B_{nospace{2}}^"*" # B_{nospace{3}}^"*" # E_{nospace{1}}^"*" # E_{nospace{2}}^"*"} right]_{nospace{}} `right rangle ~=~ left langle {bold "C"} cdot {bold "C"}^"*" lsup{"T"} right rangle, {bold "C"} ~=~ ~left[ matrix{ {bold "B"}_{LFR} ## {bold "E"}_{LFR} } right] ~ = ~left[ matrix{ {overline overline bold "M"}_{BH} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{ED}} right] cdot~ left[ matrix{ {bold "H"} ## {bold "D"}} right],

with

and the symbol T the transposition operator. Which reads:

{bold "SM"}^"L1" ~=~ left[ matrix{ {overline overline bold "M"}_{BH} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{ED}} right] ~cdot~ left langle left[ matrix{ {bold "H"} ## {bold "D"}} right] cdot left[ matrix{ {bold "H"}lsup{"T"}^"*" # {bold "D"lsup{"T"}^"*"}} right] right rangle ~cdot~ left[ matrix{ {overline overline bold "M"}_{BH}lsup{"T"}^"*" # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{ED}lsup{"T"}^"*"} right] newline dlrarrow ~ {bold "SM"}^"L2" ~=~ left langle ~left[ matrix{ H_{nospace{1}} ## H_{nospace{2}} ## H_{nospace{3}} ## D_{nospace{Y'}} ## D_{nospace{Z'}} } right] cdot left[ matrix{H_{nospace{1}}^"*" # H_{nospace{2}}^"*" # H_{nospace{3}}^"*" # D_{nospace{Y'}}^"*" # D_{nospace{Z'}}^"*"} right]_{nospace{}} `right rangle ~=~ left[ matrix{ {overline overline bold "M"}_{BH}^{-1} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{ED}^{-1}} right] ~cdot~ {bold "SM"}^"L1" ~cdot~ left[ matrix{ {overline overline bold "M"}_{BH}lsup{"T"}^{-1"*"} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{ED}lsup{"T"}^{-1"*"}} right]

(5)

since : ({overline overline bold "M"}lsup{"T"}^{"*"})^{-1} = ({overline overline bold "M"})^{-1"*"}lsup{"T"}.

3.2. Magnetic field data in SCM B1-B2-B3 axis system and electric field data in ANT V12-V23 axis system, and no calibration in V/m

If we do not want to calibrate the electric field data up to the physical ANT level (V/m), but only up to the input BIAS level (what in fact has been done so far), one can skip the ANT calibration step in Eq. (4) and only use {overline overline bold "M"}_{EV} ~=~ {overline overline bold "M"}_{EK} cdot {overline overline bold "M"}_{KV} instead of {overline overline bold "M"}_{ED} ~=~ {overline overline bold "M"}_{EK} cdot {overline overline bold "M"}_{KV} cdot {overline overline bold "M"}_{VD}. Which gives instead of Eq. (5):

{bold "SM"}^"L2" ~=~ left langle ~left[ matrix{ H_{nospace{1}} ## H_{nospace{2}} ## H_{nospace{3}} ## V_{nospace{12}} ## V_{nospace{23}} } right] cdot left[ matrix{H_{nospace{1}}^"*" # H_{nospace{2}}^"*" # H_{nospace{3}}^"*" # V_{nospace{12}}^"*" # V_{nospace{23}}^"*"} right]_{nospace{}} `right rangle ~=~ left[ matrix{ {overline overline bold "M"}_{BH}^{-1} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{EV}^{-1}} right] ~cdot~ {bold "SM"}^"L1" ~cdot~ left[ matrix{ {overline overline bold "M"}_{BH}lsup{"T"}^{-1"*"} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{EV}lsup{"T"}^{-1"*"}} right]

(6)

3.3. Magnetic and electric field data in ANT Y’-Z’ SRF

If we want to calibrate the magnetic field data in the same coordinate system as the one used for the electric field data, that is, the SRF’ frame of reference, it is also necessary to consider the transformation from the SCM B1-B2-B3 axis system to that common reference frame:

        left[ matrix{ H_nospace{X'}(%ioméga) ## H_nospace{Y'}(%ioméga) ## H_nospace{Z'}(%ioméga)} right]_nospace{SRF'} ~=~ {overline overline bold "M"}_nospace{SRF'-SCM} ~cdot~ left[ matrix{ H_{1}(%ioméga) ## H_{2}(%ioméga) ## H_{3}(%ioméga)} right]_{SCM} , {overline overline bold "M"}_nospace{SRF'-SCM} ~=~ left[ matrix{ m_nospace{X'1} # m_nospace{X'2} # m_nospace{X'3} ## m_nospace{Y'1} # m_nospace{Y'2} # m_nospace{Y'3} ## m_nospace{Z'1} # m_nospace{Z'2} # m_nospace{Z'3} } right]

In practice we will consider :
{overline overline bold "M"}_nospace{SRF'-SCM} ~simeq~ {overline overline bold "M"}_nospace{SRF-UARF} `cdot` {overline overline bold "M"}_nospace{UARF-SCM},

as given by Eq. (3). The calculation made in point 3.1. can thus be easily extended, taking into account an additional matrix multiplication, by replacing

     {overline overline bold "M"}_{BH} ~=~ {overline overline bold "M"}_{BJ} cdot {overline overline bold "M"}_{JH},

as given by Eq. (2), by

        {overline overline bold "M"}_{BH"+"} ~=~ {overline overline bold "M"}_{BJ} cdot {overline overline bold "M"}_{JH} cdot {overline overline bold "M"}_nospace{SRF'-SCM}^{-1},	(7)

which yields instead of Eq. (5):

{bold "SM"}^"L2" ~=~ left langle ~left[ matrix{ H_{nospace{X'}} ## H_{nospace{Y'}} ## H_{nospace{Z'}} ## D_{nospace{Y'}} ## D_{nospace{Z'}} } right] cdot left[ matrix{H_{nospace{X'}}^"*" # H_{nospace{Y'}}^"*" # H_{nospace{Z'}}^"*" # D_{nospace{Y'}}^"*" # D_{nospace{Z'}}^"*"} right]_{nospace{}} `right rangle ~=~ left[ matrix{ {overline overline bold "M"}_{BH"+"}^{-1} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{ED}^{-1}} right] ~cdot~ {bold "SM"}^"L1" ~cdot~ left[ matrix{ {overline overline bold "M"}_{BH"+"}lsup{"T"}^{-1"*"} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {overline overline bold "M"}_{ED}lsup{"T"}^{-1"*"}} right]

(8)

4. Onboard frame transformation and intercalibration for BP1 (& BP2 ?) computations

4.1 Transformation into SRF’ and calibration of the magnetic field fluctuations (δB)

Eq. (7) is equivalent to: {overline overline bold "M"}^{-1}_{BH"+"} ~=~ {overline overline bold "M"}_nospace{SRF'-SCM} cdot {overline overline bold "M"}^{-1}_{JH} cdot {overline overline bold "M"}^{-1}_{BJ}

Let’s normalize the SCM tranfer matrix with the TF of the coil B1 (Y axis in UARF):
{overline overline bold "M"}_{JH}(%ioméga) ~=~ C_{nospace{11}}(%ioméga) `times` {overline overline bold "c"}(%ioméga) ~=~ C_{nospace{11}}(%ioméga) left[ matrix{ 1 # c_{nospace{12}}(%ioméga) # c_{nospace{13}}(%ioméga) ## c_{nospace{21}}(%ioméga) # c_{nospace{22}}(%ioméga) # c_{nospace{23}}(%ioméga) ## c_{nospace{31}}(%ioméga) # c_{nospace{32}}(%ioméga) # c_{nospace{33}}(%ioméga)} right]_{SCM},

and approximate the LFR transfer matrix as:
{overline overline bold "M"}_{BJ} ~approx~ R_{SCM}(%ioméga ) `times` left [ matrix{1 # 0 # 0 ## 0 # 1 # 0 ## 0 # 0 # 1} right],
R_{SCM} ~=~ R_{nospace{11}}^{SCM} approx R_{nospace{22}}^{SCM}approx R_{nospace{33}}^{SCM}
       with

Hence:
{overline overline bold "M"}^{-1}_{BH"+"} ~=~ {1 over {C_{nospace{11}}(%ioméga)R_{SCM}(%ioméga) }} ~times~ {overline overline bold "M"}_nospace{SRF'-SCM} cdot left[{overline overline bold "c"}^{-1}(%ioméga)right]_{SCM}
        (9)

{tilde overline overline bold "M"}_nospace{SRF'-SCM}(%ioméga) ~=~ left[ matrix{ {tilde m}_nospace{X'1} # {tilde m}_nospace{X'2} # {tilde m}_nospace{X'3} ## {tilde m}_nospace{Y'1} # {tilde m}_nospace{Y'2} # {tilde m}_nospace{Y'3} ## {tilde m}_nospace{Z'1} # {tilde m}_nospace{Z'2} # {tilde m}_nospace{Z'3} } right](%ioméga)

Let's note the matrix above the brace by:

4.2 Transformation into SRF’ and calibration of the electric field fluctuations (δE)

Similar calculation can be made for the electric field signals. From Eq. (4) we get:

        {overline overline bold "M"}^{-1}_{ED} ~=~ {overline overline bold "M"}^{-1}_{VD} cdot {overline overline bold "M"}^{-1}_{KV} cdot {overline overline bold "M"}^{-1}_{EK}

where:
{overline overline bold "M"}_{EK}(%ioméga) ~approx~ R_{BIAS}(%ioméga ) `times` left [ matrix{1 # 0 ## 0 # 1} right], with R_{BIAS} ~=~ R_{nospace{11}}^{BIAS} approx R_{nospace{22}}^{BIAS}
{overline overline bold "M"}_{KV}(%ioméga) ~approx~ B(%ioméga ) `times` left [ matrix{1 # 0 ## 0 # 1} right], with B ~=~ B_{nospace{11}} approx B_{nospace{22}}
{overline overline bold "M"}_{VD}^{-1}(%ioméga) ~=~ size18{alignc 1 over {A_{nospace{1Y'}}A_{nospace{2Z'}}-A_{nospace{1Z'}}A_{nospace{2Y'}}}} left[ matrix{ A_{nospace{2Z'}}(%ioméga) # -A_{nospace{1Z'}}(%ioméga) ## -A_{nospace{2Y'}}(%ioméga) # A_{nospace{1Y'}}(%ioméga)} right]_{nospace{SRF'}}
Hence:
{overline overline bold "M"}^{-1}_{ED} ~=~ {1 over sqrt{lline A_nospace{2Y'} rline^2 + lline A_nospace{2Z'} rline^2}}{1 over { B(%ioméga)R_{BIAS}(%ioméga) }} ~times~ sqrt{lline A_nospace{2Y'} rline^2 + lline A_nospace{2Z'} rline^2} times{overline overline bold "M"}^{-1}_{VD}
        (10)

{tilde overline overline bold "A"}_nospace{SRF'-ANT}(%ioméga) ~=~ left[ matrix{ {tilde a}_nospace{Y'1} # {tilde a}_nospace{Y'2} ## {tilde a}_nospace{Z'1} # {tilde a}_nospace{Z'2} } right](%ioméga)
Let's note the matrix above the brace by:

4.3 Coefficients to be transmitted for onboard transformation and calibration of δB and δE
In fact, we currently believe that it is possible to calibrate the ASM products first and then compute the BP products, which means a more accurate computation of the average spectral products over the frequency bins.
As we aim at combining the electric and magnetic field measurements for determining the Poynting flux SX’ and the phase velocity VPHI, we need a cross-calibration factor between them. Substituting Eqs. (9) and (10) in Eq. (8), we propose the following factorization:

{bold "SM"}^"L2" =` left langle left[ matrix{ {bold "H"} ## {bold "D"}} right] cdot left[ matrix{ {bold "H"} ## {bold "D"}} right]lsup{"T"}^"*" right rangle_{SRF'} =` {%kappa`}^{2} ` left[ matrix{{%alpha} over {%kappa} {tilde overline overline bold "M"}_nospace{SRF'-SCM} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {%beta} over {%kappa} {tilde overline overline bold "A"}_nospace{SRF'-ANT}} right] `cdot` {bold "SM"}^"L1" cdot` left[ matrix{ {%alpha^{"*"}} over {%kappa} {tilde overline overline bold "M"}_nospace{SRF'-SCM}lsup{"T"}^{"*"} # matrix{0 # 0 ## 0 # 0 ## 0 # 0} ## matrix{0 # 0 #0 ## 0 # 0 # 0} # {%beta^{"*"}} over {%kappa} {tilde overline overline bold "A"}_nospace{SRF'-ANT}lsup{"T"}^{"*"}} right]

(11)

stack{ %alpha ~=~ {~~~~~~~1} over { C_{nospace{11}}(%ioméga)R_{SCM}(%ioméga) } # %beta ~=~ {~~~~~~~1} over sqrt{lline A_nospace{2Y'} rline^2 + lline A_nospace{2Z'} ~ rline^2} `{~~~~~~1} over { B(%ioméga)R_{BIAS}(%ioméga)} }

        with

and %kappa(F) `=` 1e-4 (for simplicity, here we have chosen no dependence with F=0, 1, 2), a numerical constant for the onboard calibrated ASM products to match the digital output dynamics of the LFR, i.e. their magnitudes should be between 2-27 and 237.

What we must then transmit for a given set of frequencies for the calibration of the ASM on board and the subsequent calculation of the BP1 and BP2, are :
a) The 9 complex components (18 floats):

{%alpha(%omega)} over {%kappa} ~ {tilde m}_nospace{ij}(%omega) with i = X’, Y’, Z’ and j = 1, 2, 3
which allow the calibration and transformation of the magnetic field fluctuations into SRF’,
b) The 4 complex components (8 floats):
{%beta(%omega)} over {%kappa} `times` {tilde a}_nospace{ij}(%omega)
      with i = Y’, Z’ and j = 1, 2

which allow the calibration and transformation of the electric field fluctuations into SRF’ and, thus, their amplitude and phase cross-calibration with the magnetic field fluctuations.
They determine a new set of “k-coefficients” and make a total of 18 + 8 = 26 floats by bin, which is fine because up to 32 floats by bin can be implemented. As 12 + 13 +11 = 36 frequency bins are allowed, we will add 1 more frequency bin by F-channel, in order to implement in a simple way a linear interpolation of the coefficients to calibrate the ASM to the specified 12*8 + 13*8 +11*8 = 36*8 frequency bins.