# General
Port 0 = internal configuration port
Port 1 = external port
Port 2 = external port
Port 3 = USB

## Router mode
first byte of each packet is used to determine the destination of the packet
see the “SpaceWire Configuration library software manual”
## Node mode
all data received from SpaceWire ports is routed to port 3
the first byte of the packet is still use to address the port that the packet is to be sent out of
## Network mode and Header mode
The Network mode allows to send TCP/IP packets over the SpaceWire network. When writing packets using the SpaceWire USBAPI, it is normally necessary to disable bit Network and Header modes. The Header mode is OFF by default.

void USBSpaceWire_EnableNetworkMode(star_device_handle hDevice, char bEnable);
# RMAP Configuration
The use of RMAP must be specifically enabled by calling CFGSpaceWire_EnableRMAP. Note that calling this function just affects the operations performed by the Configuration Library and does not affect the packets sent and received using the driver API.
To configure a device connected to the PC by USB the path is 0, 254 and the return path is 254.
The destination key should always be 0x20 (32 decimal) for STAR-Dundee devices.
The Remote Memory Access Protocol (RMAP) must be used when configuring all STAR-Dundee
devices purchased since 2006.
Configuration with RMAP must be enabled, which will cause all configuration operations to be sent as RMAP packets. This does not affect other packets sent using the USB API.

Int CFGSpaceWire_SetAsInterface(star_device_handle hDevice, char bEnabled, char bAddIdentifier);

This function enables or disables the device as an interface. When enabled as an interface all packets received into the device on the SpaceWire links will be routed out of the external port, the USB port on the SpaceWire USB devices. If not enabled as an interface the device will act as a router, routing packets based on the first byte.

In order to receive packets on a particular star_device_handle, that star_device_handle must first register to receive packets on a particular port, or on all ports. This can be achieved by calling

USBSpaceWire_RegisterReceiveOnPort()

to receive on a specific port, or

USBSpaceWire_RegisterReceiveOnAllPorts()

to receive on all ports. A port in these functions refers to the first byte of the packet received. This can be useful for receiving from a specific link from a SpaceWire USB Device, as these devices can be set to operate as interfaces, adding a byte containing the link number on which each packet is received to the front of packets.

Address Range	Function
0	Internal Configuration Port
1-31 (01-1F hex)	Physical Output Ports
32-254 (20-FE hex)	Logical Addresses, which are mapped on to the physical output ports.
255 (FF hex)	Reserved